## Slide 1
vPIM: Efficient Virtual Address Translation for Scalable Processing-in-Memory Architectures
Amel Fatima, Sihang Liu, Korakit Seemakhupt, Rachata Ausavarungnirun, Samira Khan
Notes: Hi Everyone, I am Amel Fatima and today I am going to talk about our work on “vPIM: An efficient address translation mechanism for PIM architectures”

## Slide 2: Summary
  Multiple PIM stacks provide increase capacity for emerging data-intensive workloads
Problem: Address translation incurs significant overhead in accessing multiple PIM stacks
    Radix-based translation: Multiple sequential cross-stack page table walks
    Cuckoo hash-based translation: Multiple parallel accesses across memory stacks
Goal: Design an efficient address translation scheme for multi-stack PIM systems
Observations and Key Ideas:
  Observation: High intra-stack parallelism with multiple vaults in each stack
  Key Idea: Network-contention-aware hash
    Change cuckoo hash layout to generate parallel accesses within one stack across multiple vaults
    Send only one request towards the stack and generate parallel accesses within the stack
  Observation: High parallelism enables minimal performance loss with fewer cores
  Key Idea: Pre-translate addresses
    Use a few cores to run ahead future iterations of the workload
    Pre-translate cross-stack addresses and bring them inside the same stack for future use
Result: vPIM provide 4.4x and 1.7x speedup compared to radix and cuckoo hash
Notes:   I WILL start by briefly summarizing our work. Processing in memory PIM is a new technology that brings computation closer to the memory. To further satisfy the demand of data intensive applications multiple PIM stacks are connected over a memory network to scale the capacity. Performing address translation in such multi-stack pIM systems incur additional overhead as a result of making multiple cross stack accesses over the network. For example in a radix based translation, we make multiple sequential cross stack accesses to retrieve the translation whereas in a recently proposed cuckoo hash based transaltion we make parallel accesses across the network. So in this work, our goal is to design an efficient address translation scheme for such multi-stacked PIM systems. To achieve our goal, we make a few observations and based on those we propose our two main key ideas. Our first observation is the presence of high intra stack parallelism with multiple vaults within each stack. BASED ON that, we propose our network contention aware hash which spawns parallel accesses within a stack by sending only one request across the network. Our second observation of high core parallelism which enables minimal performance loss with fewer cores leads to our second key idea of pretranslation. This involves dedicating some cores in a stack to run ahead future iterations of the workloads. By running future iterations we pre-translate page table walks and bring them inside the stack for future use. Our proposal achieves a 4.4 times 1.7 times speedup compared to radix and cuckoo hash.

## Slide 3: Outline
Processing-in-Memory Introduction
Address Translation in PIM Architecture
Challenges and Key Ideas
Evaluation
Conclusion
Notes: This is a brief outline of todays talk. I will st

## Slide 4: Outline
Processing-in-Memory Introduction
Address Translation in PIM Architecture
Challenges and Key Ideas
Evaluation
Conclusion
Notes: I will start by introducing processing-in-memory architecture.

## Slide 5: Processing in Memory (PIM)
PIM is a new technology where computation is placed closer to the memory
Notes: PIM is a new technology where

## Slide 6: Processing in Memory (PIM)
PIM is a new technology where computation is placed closer to the memory
Vault 0
Vault 31
Multiple
Memory Banks
Vault 0
Vault 0
Vault 0
Vault 0
Notes: computation *
is placed

## Slide 7: Processing in Memory (PIM)
PIM is a new technology where computation is placed closer to the memory
Vault 0
Core 0
Vault Logic
…
Vault 31
Core 31
Vault Logic
PIM STACK
HOST CPU
PIM STACK
Multiple
Memory Banks
Core 0
Vault Logic
Vault 0
Vault 0
Vault 0
Vault 0
Notes: closer to the memory * in order to reduce the data movement bottleneck in current systems.

## Slide 8: Processing in Memory (PIM)
PIM is a new technology where computation is placed closer to the memory
Vault 0
Core 0
Vault Logic
…
Vault 31
Core 31
Vault Logic
Prior works used PIM to reduce data movement between CPU and memory
  Tesseract[ISCA’15], Tetris[ASPLOS’17], TOM[ISCA’16], etc.
PIM STACK
HOST CPU
PIM STACK
Multiple
Memory Banks
Core 0
Vault Logic
Vault 0
Vault 0
Vault 0
Vault 0
Notes: *There are several prior works that leverage PIM capability to enhance performance.

## Slide 9: Processing in Memory (PIM)
PIM is a new technology where computation is placed closer to the memory
Vault 0
Core 0
Vault Logic
…
Vault 31
Core 31
Vault Logic
Prior works used PIM to reduce data movement between CPU and memory
  Tesseract[ISCA’15], Tetris[ASPLOS’17], TOM[ISCA’16], etc.
PIM STACK
HOST CPU
PIM STACK
Multiple
Memory Banks
Core 0
Vault Logic
Vault 0
Vault 0
Vault 0
Vault 0
Placing computation closer to memory improves performance
Notes: . *So placing computation closer to the memory improves performance.

## Slide 10: Processing in Memory (PIM)
Data-intensive applications demand more memory
Vault 0
Core 0
Vault Logic
…
Vault 31
Core 31
Vault Logic
PIM STACK
Multiple
Memory Banks
Core 0
Vault Logic
Vault 0
Vault 0
Vault 0
Vault 0
Notes: : Data-intensive applications demand more memory. To satisfy the demand of such emerging data intensive applications

## Slide 11: Processing in Memory (PIM)
Data-intensive applications demand more memory
Vault 0
Core 0
Vault Logic
…
Vault 31
Core 31
Vault Logic
PIM STACK
Multiple
Memory Banks
Core 0
Vault Logic
Vault 0
Vault 0
Vault 0
Vault 0
Multiple stacks are connected over a memory network to scale up to higher capacity
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
Host CPU
S11
S12
S15
S10
S13
S14
Notes: multiple PIM stacks are connected over a memory network to scale up to higher capacity.

## Slide 12: Processing in Memory (PIM)
Data-intensive applications demand more memory
Vault 0
Core 0
Vault Logic
…
Vault 31
Core 31
Vault Logic
PIM STACK
Multiple
Memory Banks
Core 0
Vault Logic
Vault 0
Vault 0
Vault 0
Vault 0
Multiple stacks are connected over a memory network to scale up to higher capacity
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
Host CPU
S11
S10
S15
S12
S13
S14
A multi-stacked PIM system provides increased capacity
for emerging data-intensive applications
Notes: A multi-stacked PIM system provides increased capacity for emerging data intensive applications

## Slide 13: Outline
Processing-in-Memory Introduction
Address Translation in PIM Architecture
Challenges and Key Ideas
Evaluation
Conclusion
Notes: Now I will talk about address translation in such multi-stacked PIM architectures

## Slide 14: Memory Management in PIM
Vault 0
Core 0
Vault Logic
…
Vault 31
Core 31
Vault Logic
PIM STACK
Multiple
Memory Banks
Core 0
Vault Logic
Vault 0
Vault 0
Vault 0
Vault 0
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
Host CPU
Access from CPU Host
S11
S10
S12
S13
S15
S14
Notes: The execution of an application is divided between the CPU and PIM cores

## Slide 15: Memory Management in PIM
Vault 0
Core 0
Vault Logic
…
Vault 31
Core 31
Vault Logic
PIM STACK
Multiple
Memory Banks
Core 0
Vault Logic
Vault 0
Vault 0
Vault 0
Vault 0
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
Host CPU
Both CPU and PIM cores are accessing the same memory
Access from CPU Host
Access from PIM cores
S11
S10
S15
S12
S13
S14
Notes: and thus Both CPU and PIM cores access the same memory *

## Slide 16: Memory Management in PIM
PIM provides an opportunity for a unified virtual address space
Vault 0
Core 0
Vault Logic
…
Vault 31
Core 31
Vault Logic
PIM STACK
Multiple
Memory Banks
Core 0
Vault Logic
Vault 0
Vault 0
Vault 0
Vault 0
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
Host CPU
Both CPU and PIM cores are accessing the same memory
Access from CPU Host
Access from PIM cores
S11
S10
S12
S13
S14
S15
Notes: This setting provides an opportunity for a unified virtual address space between the CPU and PIM cores

## Slide 17: Address Translation
Notes: .

## Slide 18: Address Translation
Unified virtual memory requires translating virtual addresses to physical addresses
Virtual Address
Translation
Physical Address
Notes: * A unified virtual memory requires translating virtual addresses to physical addresses * .

## Slide 19: Address Translation
Unified virtual memory requires translating virtual addresses to physical addresses
Address translation requires multiple accesses to the page table
Virtual Address
Translation
Physical Address
Notes: * This Address translation requires making multiple accesses to the page table

## Slide 20: Address Translation
Unified virtual memory requires translating virtual addresses to physical addresses
Address translation requires multiple accesses to the page table
It introduces significant overhead in conventional systems which is even worse in PIM
Virtual Address
Translation
Physical Address
Notes: These accesses incurs significant overhead in a conventional system which is even worse in a PIM based system.

## Slide 21: Address Translation
Unified virtual memory requires translating virtual addresses to physical addresses
Address translation requires multiple accesses to the page table
It introduces significant overhead in conventional systems which is even worse in PIM
There are two different commonly used approaches for address translation:
Virtual Address
Translation
Physical Address
Notes: * There are two commonly used approaches of translating virtual addresses in current systems:

## Slide 22: Address Translation
Unified virtual memory requires translating virtual addresses to physical addresses
Address translation requires multiple accesses to the page table
It introduces significant overhead in conventional systems which is even worse in PIM
There are two different commonly used approaches for address translation:
  Radix Page Table
Virtual Address
Translation
Physical Address
Notes: * Radix page table based approach
*

## Slide 23: Address Translation
Unified virtual memory requires translating virtual addresses to physical addresses
Address translation requires multiple accesses to the page table
It introduces significant overhead in conventional systems which is even worse in PIM
There are two different commonly used approaches for address translation:
  Radix Page Table
  Hash Page Table
Virtual Address
Translation
Physical Address
Notes: Hash page table based approach

## Slide 24: Address Translation
Unified virtual memory requires translating virtual addresses to physical addresses
Address translation requires multiple accesses to the page table
It introduces significant overhead in conventional systems which is even worse in PIM
There are two different commonly used approaches for address translation:
  Radix Page Table
  Hash Page Table
Virtual Address
Translation
Physical Address
Both radix and hash page table introduce
significant overhead in multi-stacked PIM system
Notes: Both radix and hash page table translation incur significant overhead in a PIM based system.
* Now I will discuss about these two mechanisms one by one and talk about their integration overhead in a PIM system.

## Slide 25: Radix Based Address Translation
A virtual address is translated to a physical address by walking 4 levels of page table
Virtual Address
Translation
Physical Address
Notes: The first one is the radix based translation,

## Slide 26: Radix Based Address Translation
A virtual address is translated to a physical address by walking 4 levels of page table
Virtual Address
Translation
Physical Address
Notes: In a radix based page table walk a virtual address is translated to a physical address

## Slide 27: Radix Based Address Translation
A virtual address is translated to a physical address by walking 4 levels of page table
Virtual Address
47:39
CR3
38:30
29:21
20:12
L3
PPN
Virtual Address
Translation
Physical Address
L4
L2
L1
Notes: by making four sequential accesses to the page table

## Slide 28: Radix Based Translation in PIM
Notes: Now I will talk about integrating this radix page table walk in a PIM based system.

## Slide 29: Radix Based Translation in PIM
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
Page Tables are distributed across the PIM stacks
S10
S11
Notes: * In a PIM based system, radix page table is distributed across the PIM stacks. Therefore

## Slide 30: Radix Based Translation in PIM
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
Page Tables are distributed across the PIM stacks
Each translation can require up to four accesses to different PIM stacks
S10
Virtual Address
47:39
CR3
L4
38:30
29:21
20:12
S11
TLB Miss at Stack 5
Notes: . EACH TRANSLATION access may require making four sequential accesses to different PIM stacks. *

## Slide 31: Radix Based Translation in PIM
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
Page Tables are distributed across the PIM stacks
Each translation can require up to four accesses to different PIM stacks
S10
Virtual Address
47:39
CR3
L4
38:30
29:21
20:12
L3
S11
TLB Miss at Stack 5

## Slide 32: Radix Based Translation in PIM
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
Page Tables are distributed across the PIM stacks
Each translation can require up to four accesses to different PIM stacks
S10
Virtual Address
47:39
CR3
L4
38:30
29:21
20:12
L3
L2
S11
TLB Miss at Stack 5

## Slide 33: Radix Based Translation in PIM
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
Page Tables are distributed across the PIM stacks
Each translation can require up to four accesses to different PIM stacks
S10
Virtual Address
47:39
CR3
L4
38:30
29:21
20:12
L3
L2
L1
PPN
S11
TLB Miss at Stack 5

## Slide 34: Radix Based Translation in PIM
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
Page Tables are distributed across the PIM stacks
Each translation can require up to four accesses to different PIM stacks
S10
Virtual Address
47:39
CR3
L4
38:30
29:21
20:12
L3
L2
L1
PPN
S11
TLB Miss at Stack 5
A single radix page walk can introduce
sequential accesses to multiple memory stacks
Notes: So we can conclude that a radix page table walk can introduce sequential accesses to multiple memory stacks.

## Slide 35: Hash Based Address Translation
Hash based translation use hash table to lookup a physical address
Virtual Address
Translation
Physical Address
Notes: Now i will talk about the second commonly used approach of address translation i.e. hash based translation

## Slide 36: Hash Based Address Translation
Hash based translation use hash table to lookup a physical address
Virtual Address
Translation
Virtual Address (VA1)
VA2/PA2
Physical Address
…
H1
Notes: which requires accessing a hash table to retrieve the translation..

## Slide 37: Hash Based Address Translation
Hash based translation use hash table to lookup a physical address
Hash page table suffers from collision overhead
Virtual Address
Translation
Virtual Address (VA1)
VA2/PA2
Physical Address
Collision
…
H1
Notes: HASH page tables suffer from collision overhead

## Slide 38: Hash Based Address Translation
Hash based translation use hash table to lookup a physical address
Hash page table suffers from collision overhead
Collisions lead to multiple sequential accesses in a hash table
Virtual Address
Translation
Virtual Address (VA1)
VA2/PA2
VA1/PA1
Physical Address
Collision
…
Sequentially look for
the next entry
H1
Notes: which requires making sequential accesses in order to be resolved

## Slide 39: Hash Based Address Translation
Hash based translation use hash table to lookup a physical address
Hash page table suffers from collision overhead
Collisions lead to multiple sequential accesses in a hash table
Virtual Address
Translation
Virtual Address (VA1)
VA2/PA2
VA1/PA1
Physical Address
Collision
…
Sequentially look for
the next entry
Hash table eliminates pointer chasing but
introduces sequential accesses due to collisions.
H1
Notes: . So we can say that hash table reduces pointer chasing based ptw but introduces sequential accesses due to collisions.

## Slide 40: Alternative: Cuckoo Hash Table
Multiple parallel accesses are issued in hash table to mask the overhead of collisions
Virtual Address
Translation
Physical Address
Notes: Cuckoo hash table as used by recent prior works introduces a new collision resolution technique

## Slide 41: Alternative: Cuckoo Hash Table
Multiple parallel accesses are issued in hash table to mask the overhead of collisions
Virtual Address (VA1)
H1
H2
Virtual Address
Translation
Physical Address
Notes: that makes parallel accesses

## Slide 42: Alternative: Cuckoo Hash Table
Multiple parallel accesses are issued in hash table to mask the overhead of collisions
Virtual Address (VA1)
VA2/PA2
VA1/PA1
…
VA3/PA3
…
Virtual Address
Translation
Physical Address
H1
H2
Notes: to resolve collisions.

## Slide 43: Alternative: Cuckoo Hash Table
Multiple parallel accesses are issued in hash table to mask the overhead of collisions
Virtual Address (VA1)
VA2/PA2
VA1/PA1
Cuckoo hash table enables parallel lookups upon collisions
…
VA3/PA3
…
Virtual Address
Translation
Physical Address
H1
H2
Notes: . * Thus we can say that cuckoo hashing allows us to avoid expensive sequential memory accesses and instead enables parallel lookups upon collisions.

## Slide 44: Alternative: Cuckoo Hash Table in PIM
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
Parallel accesses are issued across different stacks in PIM
S10
…
…
TLB Miss at Stack 5
Virtual Address (VA1)
VA2/PA2
VA1/PA1
…
VA3/PA3
…
S0
S11
H1
H2
Notes: Now we will discuss the integration of cuckoo hash page table in a pIM system.

## Slide 45: Alternative: Cuckoo Hash Table in PIM
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
Parallel accesses are issued across different stacks in PIM
S10
…
…
TLB Miss at Stack 5
Virtual Address (VA1)
VA2/PA2
VA1/PA1
…
VA3/PA3
…
S0
S11
Parallel Access 1
Parallel Access 2
H1
H2
Notes: integrating cuckoo hash page table in PIM introduces parallel accesses which can be directed to different PIM stacks *

## Slide 46: Alternative: Cuckoo Hash Table in PIM
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
Parallel accesses are issued across different stacks in PIM
S10
Parallel cross-stack accesses increase network
contention and thus overall memory access time
…
…
TLB Miss at Stack 5
Virtual Address (VA1)
VA2/PA2
VA1/PA1
…
VA3/PA3
…
S0
S11
Parallel Access 1
Parallel Access 2
H1
H2
Notes: *These parallel accesses increase memory network contention and thus overall cross-stack memory access time

## Slide 47: Overhead of Hash and Radix Translation in PIM
…
…
Notes: To summarize the overhead of radix and hash page translation in PIM

## Slide 48: Overhead of Hash and Radix Translation in PIM
…
…
Notes: * this graph shows the slowdown from each approach relative to an ideal address translation. *

## Slide 49: Overhead of Hash and Radix Translation in PIM
…
…
Naïve integration of radix and cuckoo hash page table
cause significant slowdown in a PIM based system
Notes: We can conclude that naïve integraton of radix and cuckoo hash table in PIM causes significant slowdown in a PIM based system.

## Slide 50: Goal
Notes: This brings us to our goal which is to

## Slide 51: Goal
Design an efficient address translation
scheme for multi-stack PIM systems
Notes: design an efficient address transltion scheme for multi-stacked PIM systems

## Slide 52: Outline
Processing-in-Memory Introduction
Address Translation in PIM Architecture
Challenges and Key Ideas
Evaluation
Conclusion
Notes: Now we will talk about the challenges and our proposed key ideas to achieve our goal

## Slide 53: Challenge: Parallel lookups increase contention
Parallel lookups in cuckoo hash lead to increased memory network contention
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
S11
TLB Miss at Stack 5
Parallel Access 1
Parallel Access 2
Notes: Parallel lookups in cuckoo hash lead to increased memory network contention

## Slide 54: Challenge: Parallel lookups increase contention
Parallel lookups in cuckoo hash lead to increased memory network contention
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
TLB Miss at Stack 5
Parallel Access 1
Parallel Access 2
S11
Notes: The graph on the right shows average cross stack memory latency on the y axis and number of parallel accesses on the x axis. We can see that the average memory access latency is dominated by The network traversal time

## Slide 55: Challenge: Parallel lookups increase contention
Parallel lookups in cuckoo hash lead to increased memory network contention
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
TLB Miss at Stack 5
Parallel Access 1
Parallel Access 2
S11
Notes: And increases with the number of parallel accesses issued the hash table

## Slide 56: Challenge: Parallel lookups increase contention
Parallel lookups in cuckoo hash lead to increased memory network contention
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
TLB Miss at Stack 5
Parallel Access 1
Parallel Access 2
Cross-stack memory access latency
increase with parallel accesses
S11
Notes: So we can say that the average cross-stack memory access latency increase wit the number of parallel accesses

## Slide 57: Observation: Massive parallelism inside stack
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
S11
Notes: To counter that challenge we make our first observation of

## Slide 58: Observation: Massive parallelism inside stack
We observe immense intra-stack parallelism for parallel accesses
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
S11
Notes: massive parallelism inside each stack

## Slide 59: Observation: Massive parallelism inside stack
We observe immense intra-stack parallelism for parallel accesses
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
S11
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 31
Core 31
Hash Table
Vault Logic
Vault 1
Core 1
Hash Table
Vault Logic
Vault 2
Core 2
Hash Table
Vault Logic
Notes: Each stack has multiple vaults

## Slide 60: Observation: Massive parallelism inside stack
We observe immense intra-stack parallelism for parallel accesses
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
S11
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 31
Core 31
Hash Table
Vault Logic
Vault 1
Core 1
Hash Table
Vault Logic
Vault 2
Core 2
Hash Table
Vault Logic
Notes: Which can be used to trigger parallel accesses

## Slide 61: Observation: Massive parallelism inside stack
We observe immense intra-stack parallelism for parallel accesses
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
S11
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 31
Core 31
Hash Table
Vault Logic
Vault 1
Core 1
Hash Table
Vault Logic
Vault 2
Core 2
Hash Table
Vault Logic
Network traversal can be avoided if parallel accesses are
generated within the same stack and across different vaults
Notes: So we ask the question whether we can utilize the intra stack parallelism to generate parallel inside the stack to avoid expensive network traversal

## Slide 62: Key Idea: Network-contention-aware hash
Parallel lookups generated within the stack avoid costly cross-stack page table walks
S11
Notes: This brings us to our first key idea of network contention aware hash where parallel accesses are generated inside each stack

## Slide 63: Key Idea: Network-contention-aware hash
Parallel lookups generated within the stack avoid costly cross-stack page table walks
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
TLB Miss at Stack 5
S11
S11
Notes: On a TLB miss

## Slide 64: Key Idea: Network-contention-aware hash
Parallel lookups generated within the stack avoid costly cross-stack page table walks
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
TLB Miss at Stack 5
S11
Only One Access Sent
S11
Notes: We only send one access across the network and on reaching the destination stack that request

## Slide 65: Key Idea: Network-contention-aware hash
S11
Parallel lookups generated within the stack avoid costly cross-stack page table walks
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
TLB Miss at Stack 5
S11
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 31
Core 31
Hash Table
Vault Logic
Only One Access Sent
Generation of Parallel Accesses
Notes: Spawns parallel accesses inside the stack and across different vaults

## Slide 66: Key Idea: Network-contention-aware hash
S11
Parallel lookups generated within the stack avoid costly cross-stack page table walks
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
TLB Miss at Stack 5
S11
Network-contention-aware hash spawn parallel accesses
within the same stack to avoid network traversal
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 31
Core 31
Hash Table
Vault Logic
Only One Access Sent
Generation of Parallel Accesses
Notes: This way of parallel access generation ensures that we avoid expensive network traversal and reduce the network contention

## Slide 67: Benefit and Opportunity
V
N
Timeline
Vault Time
Network Time
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
S11
TLB Miss at Stack 5
N
Cuckoo hash
V
Parallel Access 1
Parallel Access 2
Parallel Access 1
Parallel Access 2
Notes: Now we will talk about the benefits and opportunities after the application of out first key idea. We had our baseline cuckoo hash which generated parallel accesses across the NETWORK leading to increased network contention.

## Slide 68: Benefit and Opportunity
V
N
Timeline
Vault Time
Network Time
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
S11
N
V
Parallel Access 1
Parallel Access 1
Parallel Access 2
Cycles Saved
N
Timeline
N
Network contention-aware hash
V
V
Parallel Access 1
Parallel Access 2
TLB Miss at Stack 5
Cuckoo hash
Notes: On top of that, we proposed our network contention aware hash which spawned parallel accesses within the stack and reduced the network contention thus reducing the overall cross-stack memory access latency

## Slide 69: Benefit and Opportunity
V
N
Timeline
Vault Time
Network Time
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
S11
N
V
Parallel Access 1
Parallel Access 1
Parallel Access 2
Cycles Saved
N
Timeline
N
Network contention-aware hash
V
V
Parallel Access 1
Parallel Access 2
Opportunity
Timeline
Opportunity to optimize
V
V
Parallel Access 1
Parallel Access 2
Can we get rid of this cross-stack access?
Cuckoo hash
Notes: After application of this , we still see that we are generating an access that is still traversing the network.

## Slide 70: Benefit and Opportunity
V
N
Timeline
Vault Time
Network Time
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
S11
N
V
Parallel Access 1
Parallel Access 1
Parallel Access 2
Cycles Saved
N
Timeline
N
Network contention-aware hash
V
V
Parallel Access 1
Parallel Access 2
Opportunity
Timeline
Opportunity to optimize
V
V
Parallel Access 1
Parallel Access 2
Is there any way to eliminate the overhead of cross-stack access?
Can we get rid of this cross-stack access?
Cuckoo hash
Notes: So we ask the question, whether we can get rid of this cross-stack access and eliminate the overhead of cross-stack accesses further

## Slide 71: Observation: PIM programs feature high parallelism
PIM suitable programs manifest as independent threads that can be assigned to different cores and execute in parallel
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
#pragma omp parallel for
for(...)
{
…
}
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Notes: To answer that question, we make another observation i.e. that PIM programs feature high parallelism

## Slide 72
PIM suitable programs manifest as independent threads that can be assigned to different cores and execute in parallel
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
#pragma omp parallel for
for(...)
{
…
}
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Iterations are evenly distributed
across the PIM stacks for computation
Observation: PIM programs feature high parallelism
Notes: PIM suitable programs manifest as independent threads that can be assigned across different stacks

## Slide 73
PIM suitable programs manifest as independent threads that can be assigned to different cores and execute in parallel
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
#pragma omp parallel for
for(...)
{
…
}
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Iterations are evenly distributed
across the PIM stacks for computation
Iterations are further distributed
across the vaults within a stack
Observation: PIM programs feature high parallelism
Notes: And further within the stack and across different vaults to be executed in parallel

## Slide 74
Reduction in throughput has minimal impact on performance
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
#pragma omp parallel for
for(...)
{
…
}
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Observation: Fewer cores cause minimal slowdown
Notes: On top of that we make another observation that reducing throughout has minimal impact on performance

## Slide 75: Page table walk overhead
Observation: PIM suitable programs feature high parallelism and manifest as independent loops that can be assigned to different cores and be executed in parallel
Observation: Reduction in throughput has minimal impact on performance
Notes: To solidify our observation, we show this graph. This graph shows the reduction in performance as we reduce the number of cores from 512 to 480

## Slide 76: Page table walk overhead
Observation: PIM suitable programs feature high parallelism and manifest as independent loops that can be assigned to different cores and be executed in parallel
Observation: Reduction in throughput has minimal impact on performance
Notes: We see that there is very slight reduction in performance as we reduce the number of cores from 512 to 480

## Slide 77: Page table walk overhead
Observation: PIM suitable programs feature high parallelism and manifest as independent loops that can be assigned to different cores and be executed in parallel
Observation: Reduction in throughput has minimal impact on performance
Performance is bottlenecked by the page table walk overhead
Notes: However, we do see the performance gains that are possible by keeping the same reduced number of cores but elimination the page table walk overhead . This shows that the performance is bottlenecked by the page table walk overhead

## Slide 78: Key Idea: Pre-translation of page table walks
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
sum+=x
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Utilize some throughput to pre-translate page table walks
Code for main cores
Code for pre-translation cores
Notes: Based on these observations we propose our key idea of pre-translation of page table walks. In this key idea we propose to

## Slide 79: Key Idea: Pre-translation of page table walks
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
sum+=x
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Utilize some throughput to pre-translate page table walks
Main Cores
Pre-Translation Cores
Code for main cores
Code for pre-translation cores
Notes: Utilize some throughput to pre-translate page table walks. So in each stack we assign a fraction of the cores are pre-translation cores and the remaining cores remain the main cores performing the main computations.

## Slide 80
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
sum+=x
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Utilize some throughput to pre-translate page table walks
Main Cores
Pre-Translation Cores
Code for main cores
Pre-translation cores run ahead iterations for the main cores
Key Idea: Pre-translation of page table walks
Code for pre-translation cores
Notes: The pre-translation cores run ahead iterations for the main cores.

## Slide 81
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
sum+=x
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Filter the pre-translation code to remove non-memory accesses and accesses to small data structures that are less likely to trigger PTW
Main Cores
Pre-Translation Cores
Code for main cores
Key Idea: Pre-translation of page table walks
Code for pre-translation cores
Notes: We further propose to filter

## Slide 82
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Main Cores
Pre-Translation Cores
Code for main cores
Key Idea: Pre-translation of page table walks
Filter the pre-translation code to remove non-memory accesses and accesses to small data structures that are less likely to trigger PTW
Code for pre-translation cores
Notes: the pre-translation core’s code to ensure that they always run faster and ahead of the main cores

## Slide 83
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Code for main cores
Pre-translation cores run faster than the main cores and
are able to help a larger fraction of the main cores
Key Idea: Pre-translation of page table walks
Filter the pre-translation code to remove non-memory accesses and accesses to small data structures that are less likely to trigger PTW
Code for pre-translation cores
Notes: The graph on the extreme right shows the ratio of execution time between main and pre-translation cores per iteraton IT SHOWS THAT THE PRE-TRANSLATION CORES RUN AN ITERATION ON AVERAGE 4.2 times faster than the main cores. This also provides an opportunity for the pre-translation cores to help a relatively larger fraction of the main cores within the same stack.

## Slide 84
Code for main cores
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Main Cores
Pre-Translation Cores
Key Idea: Pre-translation of page table walks
Code for pre-translation cores
Notes: To better understand our key idea, lets do a walk through example

## Slide 85
Code for main cores
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Main Cores
Pre-Translation Cores
Step 1
Timeline
Key Idea: Pre-translation of page table walks
Code for pre-translation cores
Notes: During step 1, as the pre-translation cores are running ahead of the main cores

## Slide 86
Code for main cores
// ITERATION u =0
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Main Cores
Pre-Translation Cores
Step 1
// ITERATION u=10
u=10
Timeline
Key Idea: Pre-translation of page table walks
Code for pre-translation cores
Notes: , it starts the iteration at u=10 .

## Slide 87
Code for main cores
// ITERATION u =0
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Main Cores
Pre-Translation Cores
Step 1
u=10
TLB Miss
Generated
Timeline
Key Idea: Pre-translation of page table walks
// ITERATION u=10
Code for pre-translation cores
Notes: On executing the code within the iteration, the pre-translation core encounters a TLB miss

## Slide 88: Key Idea: Pre-translation of page table walks
Code for main cores
// ITERATION u =0
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Main Cores
Pre-Translation Cores
Step 1
u=10
TLB Miss
Generated
Perform PTW
Timeline
// ITERATION u=10
Code for pre-translation cores
Notes: To service the TLB miss, the pre-translation core performs a page table walk to get the translated address

## Slide 89
Code for main cores
// ITERATION u =0
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Main Cores
Pre-Translation Cores
Step 1
u=10
TLB Miss
Generated
Perform PTW
PB
PB
Pre-Translation Buffer
Put translated address in PB
Timeline
Key Idea: Pre-translation of page table walks
// ITERATION u=10
Code for pre-translation cores
Notes: After the page table walk is serviced, the pre-translation core stores the translation results in a pre-translation buffer located within the same stack in the pre-translation vault. This marks the end of step 1

## Slide 90: Key Idea: Pre-translation of page table walks
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Main Cores
Pre-Translation Cores
Step 1
Timeline
Pre-Translation Buffer
Step 2
Code for main cores
PB
PB
Code for pre-translation cores
Notes: Now, the step 2 starts

## Slide 91: Key Idea: Pre-translation of page table walks
Code for pre-translation cores
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Main Cores
Pre-Translation Cores
Step 1
Timeline
// ITERATION u=20
// ITERATION u =10
Pre-Translation Buffer
Step 2
u=10
Code for main cores
PB
PB
Notes: When the main core encounters the same iteration u=10 at a later point of execution

## Slide 92: Key Idea: Pre-translation of page table walks
Code for pre-translation cores
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Main Cores
Pre-Translation Cores
Step 1
Timeline
// ITERATION u=20
// ITERATION u =10
Pre-Translation Buffer
Step 2
TLB Miss
Generated
Code for main cores
PB
PB
Notes: On executing the code inside the iteration, the main core also generates a TLB miss for the same data.

## Slide 93: Key Idea: Pre-translation of page table walks
Code for pre-translation cores
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Main Cores
Pre-Translation Cores
Step 1
Timeline
// ITERATION u=20
// ITERATION u =10
Pre-Translation Buffer
Step 2
TLB Miss
Generated
Get translated address from PB
u=10
Code for main cores
PB
PB
Notes: Now, instead of performing a page table walk, the main core consults the pre-translation buffer within the stack . Since the pre-translation core had already translated the required address and stored it in the pre-translation buffer, therefore the main core gets the pre-transalted results from the PB

## Slide 94: Key Idea: Pre-translation of page table walks
Code for pre-translation cores
#pragma omp parallel for
for(...)
{
x=array1[i]
sum+=x
}
for(...)
{
x=array1[i]
}
S0
S3
S1
S2
S8
S11
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
Vault 0
Core 0
Hash Table
Vault Logic
…
Vault 29
Core 29
Hash Table
Vault Logic
Vault 30
Core 30
Hash Table
Vault Logic
Vault 31
Core 31
Hash Table
Vault Logic
Main Cores
Pre-Translation Cores
Step 1
Timeline
// ITERATION u=20
// ITERATION u =10
PB
Pre-Translation Buffer
Step 2
TLB Miss
Generated
Get translated address from PB
u=10
Pre-translation moves the page table walk
latency off the critical path of execution
Code for main cores
PB
Notes: This concludes our final step 2 and we can see that Pre-translation moves the page table walk
latency off the critical path of execution

## Slide 95: Summary of our approaches
V
N
Timeline
Vault Time
Network Time
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
S11
TLB Miss at Stack 5
N
Cuckoo hash
V
Parallel Access 1
Parallel Access 2
Parallel Access 1
Parallel Access 2
Notes: To summarize our approaches, we had our baseline cuckoo hash page table

## Slide 96: Summary of our approaches
V
N
Timeline
Vault Time
Network Time
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
S11
N
V
Parallel Access 1
Parallel Access 1
Parallel Access 2
Cycles Saved
N
Timeline
N
Network contention-aware hash
V
V
Parallel Access 1
Parallel Access 2
Cuckoo hash
Notes: On top of what we proposed our network contention aware hash that reduced network contention and thus the overall cross-stack memory access time and helped us improve our performance.

## Slide 97: Summary of our approaches
V
N
Timeline
Vault Time
Network Time
S0
S3
S1
S2
S8
S9
S4
S7
S5
S6
S12
S15
S13
S14
Host CPU
S10
S11
N
V
Parallel Access 1
Parallel Access 2
Cycles Saved
N
Timeline
N
Network contention-aware hash
V
V
Parallel Access 1
Parallel Access 2
Total Cycles Saved
PB
Network contention-aware hash
& pre-translation
Access PB in stack
Timeline
Cuckoo hash
Notes: On top of that we propose our pre-translation which further reduce the network overhead by pre-translating ptw and bringing them inside the same stack for future use.

## Slide 98: Outline
Processing-in-Memory Introduction
Address Translation in PIM Architecture
Challenges and Key Ideas
Evaluation
Conclusion
Notes: Now, I will talk about our evaluation

## Slide 99: Methodology
Configuration for Simulated PIM stacks |  | 
Memory | Total number | 16
 | Memory interconnection | Dragonfly
 | Capacity per memory | 4GB, 4 layers, 8 banks per vault
 | Vaults per memory | 32, 32 TSV per vault
 | DRAM | FR-FCFS, tCL=tRCD=tRP=17ns, tCWL=13ns
PIM Core | Type | In-order, 1 issue @ 2000MHZ
 | L1I/D-Cache | Split 32KB, 4ways, 64B cacheline, LRU, write-back, MESI
 | I/D-TLB | Split 64 entries, LRU
 | Page table walker | 1
 | Pre-Translation Buffer Size | 1024 entries per stack
Simulation Infrastructure (MultiPIM)
Notes: To model our system, we use the MultiPIM simulator which is based on already verified simulations, ramulator and zsim. The network is modelled using bookism. We evaluate a total number of 16 stacks interconnected by a dragondfly topology. Each modelled stack has 32 vaults where each vault has a single core with a TLB with 64 entries and a page table walker. Each stack had a pre-translation buffer with 1024 enties.

## Slide 100: Methodology
Workloads:
Gapbs benchmark suite with workloads:
  bfs
  tc
  cc
Parboil benchmark suite using the largest available dataset
  spmv
  sgemm
  stencil
  mri-grid
  mri-q
  histo
  tpacf
  cutcp
  lbm
  cc_sv
  sssp
  pr
Notes: We evaluate the workloads from the gapbs benchamark suite using the two real world input datasets twitter and Friendster. We also evaluate the workloads from parboil bechmakr with the largest available dataset

## Slide 101: Performance Improvement
Notes: Now talking about the performane improvement. Our Y axis shows the slowdown relative to an ideal address translation and is normalized to that. Our x axis shows the average number across all the evaluated workloads discussed before. We had our two baseline radix and cuckoo hash page table and we see that

## Slide 102: Performance Improvement
Huge performance overhead with radix and hash page table in PIM
Notes: Both of them suffer from significant performance overhead in a PIM system

## Slide 103: Performance Improvement
Notes: Our network contention aware hash on top of that helper us

## Slide 104: Performance Improvement
Network contention-aware hash achieves a speedup
of 3.97× and 1.6× compared to radix and cuckoo hash page table
Notes: Achieve a speedup of 3.97 and 1.6x compared to radix and cuckoo hash page table.

## Slide 105: Performance Improvement
Notes: On top of that we proposed our pre-translation mechanism which

## Slide 106: Performance Improvement
A total speedup of 4.4× and 1.7× is achieved
compared to radix and cuckoo hash page table
Notes: Gave us a total speedup of 4.4x and 1.7x compared to rasix and cuckoo has page table

## Slide 107: Sensitivity Results
Notes: Now we will discuss some sensitivity results as we increase the number of parallel accesses from 2 to ,4 and 8 accesses.for both cuckoo hash and our network contention aware hash.

## Slide 108: Sensitivity Results
Notes: We see that our network contention aware hash scales pretty well with 2,4, and 8 accesses

## Slide 109: Sensitivity Results
Network contention-aware hash scales well
with minor performance degradation
Notes: Showing minimal network conention introduced and thus minimal performance degradation as we increase number of paralle accesses from 2 to 8 which is a result of generating parallel accesses within a stack instead of generating them across different stacks

## Slide 110: Sensitivity Results
Notes: In addition to that we have our sensitivity results for 2 pre-translation cores and 4 pre-translation coeres epr stacks.

## Slide 111: Sensitivity Results
2 cores is a good tradeoff between
performance loss and pre-translation
Notes: We see that 2 pre-translation cores per stack is a good tradeoff between performance loss as a result of reduced number of cores for main computation and performance gain due to reduced page table walks overhead.

## Slide 112: Outline
Processing-in-Memory Introduction
Address Translation in PIM Architecture
Challenges and Key Ideas
Evaluation
Conclusion
Notes: Now I will conclude my talk.

## Slide 113: Conclusion
Multiple (PIM) stacks provide increased capacity for emerging data-intensive workloads
Running generalized applications divided between CPU and PIM is highly important
We propose address translation for multi-stack PIM running same application in CPU & PIM
Key Ideas:
  Network-contention-aware hash: Adapts cuckoo hash layout for multi-stack PIM system
  Pre-translation: Pre-translates addresses to avoid cross-stack page table walk accesses
Result: Provides 4.4x and 1.7x speedup compared to radix and cuckoo hash
Notes: .